## Slide 1: Claritas 3D REFSTAT: Refraction statics calculations

## Slide 2: Introduction:
The idea of this presentation is to provide an overview of the 3DREFSTAT utility. The presentation will give as broad overview of the step by step process used to initially generate the first break picks, input these into 3DREFSTAT, produced the Model and then the methodology to refine the model to derive the desired refraction statics for application to your seismic data.

## Slide 3: Shots with first break picks:
First break picking is carried out using the SV data viewing and analysis tool.
First breaks can be picked manually or a host of different automatic picking algorithms can be combined and parameterised to optimally pick the first breaks.

## Slide 4: 3DREFSTAT - Frontpage
Key or Required parameters are Pick Files as saved from SV after first break picking, the Geometry file, you can also provide a suitable output filename for the initial model.

## Slide 5: 3DREFSTAT – Initial basemap view
After you have confirmed the parameters on the 3DREFSTAT input form when the data has been collected the following screen will appear.
To create the Initial –
Utils Menu – Create Initial Model, The best Method to use is the 3D Grid Corners option.

## Slide 6: 3DREFSTAT – Initial model unedited
This produces a grid of squares each of which is divided into the triangles which form the model.
The model should be reasonable course to begin with say 100 to 200metres (if using feet an increment of 300 or greater), More complexity can be added as the model is refined.

## Slide 7: 3DREFSTAT – Unused triangles removed
From the UTILS menu select Delete Unused Triangles option. This removes all triangles that are not used to derive/define the model from the picks and geometry. i.e. Have no Shot / Receiver in or running through them. You can then use the Edit Verteces switch to Move/Delete or Add vertex. We recommend that under utilised Verteces are tweaked using the Move option so that they can be removed.

## Slide 8: 3DREFSTAT – Copy layer 1 to layer 2
Unused triangles for Layer 2 can also be removed using the correct option from the UTILS menu. If required additional Layers for the model can be created.

## Slide 9: 3DREFSTAT – Arrivals Window
When you have edited the Initial model such that all unused triangles have been removed. Click on the arrivals button. And the following window is generated, click the T-X button

## Slide 10: 3DREFSTAT – Arrivals window
Using the ruler option on this display you can verify suitable velocities for each of your model layers and if required update as accordingly.
Once you are happy with the initial model its worth saving it so that you can restart 3DREFSTAT at this point rather than from scratch should you need to.
Notes: <number>

## Slide 11: 3DREFSTAT – Inversion process
On the main Map interface click the calculate button which will bring up the Parameter form for the inversion process. Only the output name for the revised model is mandatory. No of iterations defaults to 2 and is probably best left at that with others best left to default.
When you OK these parameters the RMS History window will appear. This gives a visual representation of the quality of the inversion result.

## Slide 12: 3DREFSTAT – Manual updates to the model
After any of the Inversion calculation steps the

## Slide 13: Comments
The new Version of Globe Claritas (V5.6) know has an excellent suite of multiple modelling and adaptive subtraction modules providing enhanced processing capabilities to new and existing clients.