## Slide 1: WAVELET TUTORIAL GENERATION OF DESIGNATURE OPERATORS

## Slide 2: Introduction
This presentation discusses a suitable workflow for deriving and applying a minimum or zero phase designature operator from a supplied farfield airgun signature.
The farfield signature example used in this tutorial was supplied by CGGVeritas. The near trace data is from the 05CM (Crown Minerals 2005 survey), and was supplied by the NZP&M group at the Ministry of Business, Innovation and Employment NZ.
The signature was supplied at 0.5ms sample rate as an Nucleus format ASCII number dump.
The receiver ghost for the expected cable depth is modelled in WAVELET.
A debubbling filter is derived and applied to the signature.

## Slide 3: How to read a signature into the WAVELET application.
Wavelet can read either Nucleus, Gundalf native ASCII files or SegY data.
Any other ASCII format would need to be reformatted for the Wavelet application to the required WAVELET format of columns consisting of time & amplitude pairs as below:-
0.0 0.0020
0.5 -0.0020 etc
A simpler method is to use the xascsegy utility to read the ASCII text file and output a standard SegY dataset.

## Slide 4: Wavelet
The Nucleus format ASCII file is read into the WAVELET application as follows.
Start WAVELET from the launcher.
Define a name for the WAVELET session file.
WAVELET application opens, click on the NEW button.
Parameter form opens, select input text file and define T0 of the input wavelet if not identified in the input ASCII file which in this example it is.

## Slide 5: NEW wavelet parameter form

## Slide 6: Raw Farfield Signature
Notes: <number>
Raw farfield signature from Nucleus format ASCII file.
To load this into the WAVELET utility by either clicking the (NEW) button below the drop down menus or from the CREATE menu select new.
The parameter form allows you to name the input file, and annotate comments about the dataset.

## Slide 7: Receiver Ghost
.
Notes: <number>
A suitable common receiver ghost can be generated using the SPIKE option from the create menu. The user should define a positive spike (amplitude 1.0) at 0 ms and at the two way time of the expected receiver ghost a corresponding negative spike, and in this example it is at 8ms with a value of -0.9

## Slide 8: Raw Signature convolved with Rec Ghost
Notes: <number>
Using the binary menu the input signature and Receiver Ghost can be convolved.

## Slide 9: Debubble Operator
Notes: A debubble operator can be created by using the DeconOp option under the Unary menu. In this tutorial a fairly standard deconvolution for marine seismic data is used with a filter length of 220ms and a gap of 20ms.
<number>

## Slide 10: Anti-Alias Filter
Notes: <number>
The temporal anti-alias filter can be created in the WAVELET application from the create menu by selecting the butterworth filter option. The example show here is a zerophase bandpass 1-3-200-240 Hz filter suitable for resampling to 2ms.

## Slide 11: Signature with Debubble operator applied
Notes: <number>
Debubble operator convolved with the farfield signature & rec ghost output (ffsig_recghost).

## Slide 12: Signature with Debubble & AA Filter applied
Notes: <number>
Convolve the temporal anti-alias filter with the signature after debubble (ffsig_recghost_db).

## Slide 13: Signature resampled to 2ms
Notes: <number>
Resample the signature (ffsig_recghost_db_aaf) to 2ms using the Resample option from the Unary menu (NB ‘Anti-alias filter’ parameter set to ‘No’ as the butterworth filter has been applied in the previous step).
Data has also been correctly orientated at T0 using the Cell Parameters form – select ‘Cell Parameters’ option from pop up menu obtained by right clicking on the signature plot. TSTART is -63.5, TEND 436.5

## Slide 14: Minimum Phase equivalent of Signature
Notes: <number>
Minimum phase (or Zerophase) equivalent of the input signature (ffsig_resamp) can be derived by selecting the minphase (or zerophase) option from the Unary menu.

## Slide 15: Minimum Phase conversion filter
Notes: <number>
Minimum phase conversion filter - this is derived by matching (MatchFilt option in the Binary menu) the resampled signature (ffsig_resamp) to its minimum phase equivalent (ffsig_resamp_mpeq).
Save the minimum phase conversion filter to the WAVELET folder as mp_match_flt.wts - by selecting the ‘Output’ option from pop up menu obtained by right clicking on the plot.

## Slide 16: Signature with Minimum phase conv filter applied
Notes: <number>
Results of applying (Binary menu Conv option) the minimum phase conversion filter (ffsig_resamp_match) to the resampled farfield signature (ffsig_resamp).

## Slide 17: Zero Phase equivalent of Signature
Notes: <number>
Zerophase phase (or Minimum phase) equivalent of the input signature (ffsig_resamp) can be derived by selecting the zerophase (or minphase) option from the Unary menu.

## Slide 18: Zero Phase conversion filter
Notes: <number>
Zero phase conversion filter - this is derived by matching (MatchFilt option in the Binary menu) the resampled signature (ffsig_resamp) to its zero phase equivalent (ffsig_resamp_zpeq).
Save the zero phase conversion filter to the WAVELET folder as zp_match_flt.wts - by selecting the ‘Output’ option from pop up menu obtained by right clicking on the plot.

## Slide 19: Signature with Zero phase conv filter applied
Notes: <number>
Results of applying (Binary menu Conv option) the zero phase conversion filter (ffsig_resamp_match_zp) to the resampled farfield signature (ffsig_resamp).

## Slide 20: Raw Near trace data
Notes: <number>
The XSJE job flow ntr_sig_apply.job applies the minimum phase and zero phase conversion filters, saved from the WAVELET application, to a near trace plot of the survey data. In this job flow XVIEW is used to create three panels so the raw near trace data can be compared to near trace data with the minimum phase and zero phase filters applied.

## Slide 21: Min phase filter applied
Notes: <number>

## Slide 22: Zero phase filter applied
Notes: <number>

## Slide 23: Comments
WAVELET session files can be saved and returned to at a later date. Any filters or wavelets created at the point the session file is created will be regenerated when the session file is reopened.
Care should be taken in assigning the T0 point of the Farfield signature if it’s not defined in the input file. An error at this point is likely to result in a time shift being introduced when the dephasing filter is applied.